## Slide 1: WiFi Information
FOR YOUR COMPUTERS
  SSID: GEvents
  PWD: GEvents515
FOR THE MXCHIP BOARDS
  SSID: MXChipWiFi01 or MXChipWiFi02
  PWD: 12345678

## Slide 2: Sign Up for the Azure Free Trial
http://azure.com/free
If you have issues:
Open a private browser session
Sign up for a new outlook.com email address (just for today)
Enroll in the free trial using the new outlook.com account
Use that account as you go through the workshop

## Slide 3: USB STICKs
There are USB Sticks being passed around.
Please copy, not move, the contents to your computer and pass the stick on to your neighbor. Make note of the folder where you copy the content to.
The FlySimExpress folder contains the hands-on labs.
PLEASE DO NOT TAKE THE USB STICKS!
We got to a lot of effort to make these, please help make them available to future attendees!

## Slide 4: Microsoft Azure IoT Developer Kit Board
Lets you use hardware in your IoT Project prototypes without having to assemble microcontrollers and sensors and build circuits.
It provides security on board to demonstrate some hardware best practices
It let’s you focus on the value you want your IoT Solution to provide without getting mired down in the complexities of hardware.
Oh and you can deploy and debug code on the board using Visual Studio Code!
Learn more at http://aka.ms/devkit
Notes: Specs

## Slide 5: Lot’s of great projects documented

## Slide 6: Developer Tools
Microsoft Azure
Visual Studio Code

## Slide 7: FlySimExpress Lab Architecture
Presenter Creates
flysim*iot IoT Hub
Flysim*functions FlySimIoTFlightData
Raw Data
Raw Data
flysim-shared-input-hub Event Hub
Stream Analytics
flysim-shared-output-hub Event Hub
ATC UWP App
Flight Data
Flight Data (All Aircraft)
Proximity Warnings
Flight Data
Proximity Warnings
You Create
flysim*storage deviceState Table
Flight Data

## Slide 8: Full FlySim Lab Architecture
Presenter Creates
flysim-iothub-* IoT Hub
FlySimIoTFlightData Function
flysim Event Hub
FlySim UWP Client App on Windows 10
Raw Data
Raw Data
Flight Data
Flight Data
Translated Commands
flysim-shared-input-hub Event Hub
Stream Analytics
flysim-shared-output-hub Event Hub
ATC UWP App
Flight Data
Flight Data (All Aircraft)
Proximity Warnings
Flight Data
Proximity Warnings
Proximity Warnings
Translator Text API Cognitive Service
Translated Commands
Commands
Optional resources in the full workshop (http://aka.ms/flysim)
Translated Commands
You Create

## Slide 9: Full FlySim Lab Architecture
Presenter Creates
flysim-iothub-* IoT Hub
FlySimIoTFlightData Function
flysim Event Hub
FlySim UWP Client App on Windows 10
Raw Data
Raw Data
Flight Data
Flight Data
Translated Commands
flysim-shared-input-hub Event Hub
Stream Analytics
flysim-shared-output-hub Event Hub
ATC UWP App
Flight Data
Flight Data (All Aircraft)
Proximity Warnings
Flight Data
Proximity Warnings
Proximity Warnings
Translator Text API Cognitive Service
Translated Commands
Commands
Optional resources in the full workshop (http://aka.ms/flysim)
Translated Commands
You Create
Azure Storage Table
Flight Data

## Slide 10: Azure IoT Hub
Custom Cloud Gateway
Custom Cloud Gateway
Field Gateway
Device
VPN/ExpressRoute
OPC, HTTP, CoAP,…
Custom Protocols
Client SDK
IoT Edge
AMQP
Management app
Device registry/Management
Monitoring
Send commands
Client SDK
Management app
Device registry/Management
Monitoring
Send commands
Client SDK
Cloud protocol gateway sample
Cloud protocol gateway sample
AMQP, MQTT, HTTPS
Applications
Companion apps
Dashboards
Controllers
…
CoAP, AllJoyn, OPC,…
Device
Device
CoAP, AllJoyn, OPC, …
Device
Device
Device
IoT Hub
Microsoft Azure
Field Gateway

## Slide 11: IoT Hub ABC
IoT Hub
Device id
Device
C2D queue
endpoint
D2C send endpoint
Device …
Device …
Device…
IoT Hub management
Device identity management
D2C receive endpoint
Methods
endpoint
Twin endpoint
Twins endpoint
Devices Methods endpoint
Custom endpoints
C2D send and feedback endpoints
Event processing
(hot and cold path)
Event processing
(hot path)
Device management, device business logic,
Connectivity monitoring
Device provisioning and authorization
Field GW /
Cloud GW

## Slide 12: Resources
Docs.microsoft.com is the home for Microsoft technical documentation, API reference, code examples, quickstarts, and tutorials for developers and IT professionals.

## Slide 13: The Hands-On-Workshop
Open the “FlySimExpress/README.htm” from where you copied or extracted the workshop. Use the links at the bottom to get to the labs.

## Slide 14: PRESENTER ONLY - Configure Shared Resources and ATC App
flysim*iot IoT Hub
Flysim*functions FlySimIoTFlightData
Raw Data
Raw Data
flysim-shared-input-hub Event Hub
Stream Analytics
flysim-shared-output-hub Event Hub
ATC UWP App
Flight Data
Flight Data (All Aircraft)
Proximity Warnings
Flight Data
Proximity Warnings
flysim*storage deviceState Table
Flight Data
Presenter Creates
You Create
Use the Azure CLI
Use the existing ARM Template
Create the Azure Resources

## Slide 15: PRESENTER ONLY – Template Resources
flysim-shared-input-hub Event Hub
Stream Analytics
flysim-shared-output-hub Event Hub
ATC UWP App
Flight Data (All Aircraft)
Proximity Warnings
Flight Data
Proximity Warnings
{
"parameters": { "name_prefix": { "defaultValue": "name", "type": "string"} },
"variables": {
"location": "[resourceGroup().location]",
"eventHubNamespaceName": "[concat(parameters('name_prefix'),'ns')]",
"flySimSharedInputHubName": "flysim-shared-input-hub",
"flySimSharedOutputHubName": "flysim-shared-output-hub",
"streamAnalyticsJobName": "[concat(parameters('name_prefix'),'job')]"
},
"resources": [
{"comments": "Provision the Event Hub Namespace" …},
{"comments": "Provision the flysim-shared-input-hub" …},
{"comments": "Provision the Stream Analytics Job",
"properties": {
"inputs": [ { "name": "FlightDataInput" …} ],
"transformation": {
"query": “… SELECT plane1, plane2, distance INTO FlightDataOutput FROM Results"
}
"outputs": [ {"name": "FlightDataOutput"}]
}
},
{"comments": "Provision the flysim-shared-output-hub" …},
],
"outputs":{}
}
Event Hub Namespace

## Slide 16: 01 - Prepare the Azure IoT Development Kit Board
flysim*iot IoT Hub
Flysim*functions FlySimIoTFlightData
Raw Data
Raw Data
flysim-shared-input-hub Event Hub
Stream Analytics
flysim-shared-output-hub Event Hub
ATC UWP App
Flight Data
Flight Data (All Aircraft)
Proximity Warnings
Flight Data
Proximity Warnings
flysim*storage deviceState Table
Flight Data
Presenter Creates
You Create
Connect the board to WiFi
Upgrade the Firmware on it
Install the DevKit on your workstation

## Slide 17: 02 - Deploy and Verify Your Resources to Azure
flysim*iot IoT Hub
Flysim*functions FlySimIoTFlightData
Raw Data
Raw Data
flysim-shared-input-hub Event Hub
Stream Analytics
flysim-shared-output-hub Event Hub
ATC UWP App
Flight Data
Flight Data (All Aircraft)
Proximity Warnings
Flight Data
Proximity Warnings
flysim*storage deviceState Table
Flight Data
Presenter Creates
You Create
Use the Azure CLI
Use the existing ARM Template
Create the Azure Resources

## Slide 18: 03 - Deploy Your Function Code to Azure
flysim*iot IoT Hub
Flysim*functions FlySimIoTFlightData
Raw Data
Raw Data
flysim-shared-input-hub Event Hub
Stream Analytics
flysim-shared-output-hub Event Hub
ATC UWP App
Flight Data
Flight Data (All Aircraft)
Proximity Warnings
Flight Data
Proximity Warnings
flysim*storage deviceState Table
Flight Data
Presenter Creates
You Create
Deploy the function code using git
Provide the connection to the presenters shared input hub

## Slide 19: 03 - Deploy Your Function Code to Azure
flysim*iot IoT Hub
Flysim*functions FlySimIoTFlightData
Raw Data
Raw Data
flysim-shared-input-hub Event Hub
Stream Analytics
flysim-shared-output-hub Event Hub
ATC UWP App
Flight Data
Flight Data (All Aircraft)
Proximity Warnings
Flight Data
Proximity Warnings
flysim*storage deviceState Table
Flight Data
Presenter Creates
You Create
Upload the code to the board
Start publishing data
Watch the data flow

## Slide 20: Connection String
https://aka.ms/FlySimConnection

## Slide 21: DevKit Board
MCU
STM32F412
Wi-Fi
BCM43362
Audio Codec Chip
OLED
Button A
RGB LED
Security Chip
ST-SAFE A100
Edge Connector
Microphone
Headphone Jack
IrDA
MicroUSB
Power LED
3.3V DC-DC
Reset Button
Programming LED
DAP Link Chip
STMF103
Button B
Wi-Fi LED
Azure LED
User LED
Accelerometer & Gyroscope
Magnetometer
Pressure
Humidity & Temperature
GROUPED TEXT, LINES and PICTURE
SINGLE IMAGE